## Slide 1: The Coding School’s 2020 Quantum Computing Summer Camp
Hands-on learning
Day 1: Intro to Boolean logic and classical circuits

## Slide 2: Basic gates repertoire

## Slide 3: NOT gate (1 input gate)
IN | OUT
0 | 1
1 | 0
Truth table

## Slide 4: AND gate
IN 1 | IN 2 | OUT
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth table

## Slide 5: NAND gate
IN 1 | IN 2 | OUT
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
=

## Slide 6: OR gate
IN 1 | IN 2 | OUT
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 7: NOR gate
IN 1 | IN 2 | OUT
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
=

## Slide 8: XOR gate (Exclusive OR gate)
IN 1 | IN 2 | OUT
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 9: XOR gate (Exclusive OR gate)
Is equivalent to…
=

## Slide 10: XNOR gate
IN 1 | IN 2 | OUT
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
=

## Slide 11: Exercise: There are only so many gates…
Write down all possible combinations for 2-input 1-output gates and select those we already know.

## Slide 12: Boolean Algebra Rules
Name | AND form | OR form
Identity law |  | 
Null law |  | 
Idempotent law |  | 
Inverse law |  | 
Commutative law |  | 
Associative law |  | 
Distributive law |  | 
Absorption law |  | 
De Morgan’s law |  | 

## Slide 13: De Morgan’s Theorem

## Slide 14: De Morgan’s Laws In class exercise: (Truth table verification)
A | B |  | 
0 | 0 | 1 | 1
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
A | B |  | 
0 | 0 | 1 | 1
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 0 | 0

## Slide 15: Synthesis of Combinational Logic

## Slide 16: Functional specifications
There are many ways of specifying the function of a combinational device
If C is 1 then copy B to Z, otherwise copy A to Z
Truth tables: Concise description of the combinatorial system’s function
Boolean expressions: form an algebra whose operations are AND, OR and NOT.
Any combinational function can be specified as a truth table or an equivalent Boolean expression in terms of sum of products
C | B | A | Z
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Truth table
A
B
C
Z

## Slide 17: A design approach
C | B | A | X
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Truth table
Write out the functional specification as a truth table
Write down a Boolean expression with terms covering each ‘1’ in the output Sum of products
Wire up the gates

## Slide 18: In class-exercise: Binary adder
Design a logic circuit to compute the sum of two 1-bit bits. Have one bit (S) to output the 1-bit result and a carry-out bit (C) for the carry of the sum.
Binary Adder
Block diagram
A
B
C
A | B | Sum ( ) | Carry out (C)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 19: In class-exercise Adding two binary numbers
Sum
Carry
Solution

## Slide 20: Truth tables with “Don’t Cares”
We use an “X” or “don’t cares” to indicate that the value of a particular input is irrelevant in determining then value of the output.
C | B | A | Z
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
C | B | A | Z
0 | X | 0 | 0
0 | X | 1 | 1
1 | 0 | X | 0
1 | 1 | X | 1
X | 0 | 0 | 0
X | 1 | 1 | 1

## Slide 21: Designing a 2-input multiplexer
A multiplexer is a combinational logic circuit designed to switch one of the input lines through to a single common output line by the application of a control signal.
C | B | A | Y
0 | X | 0 | 0
0 | X | 1 | 1
1 | 0 | X | 0
1 | 1 | X | 1
X | 0 | 0 | 0
X | 1 | 1 | 1

## Slide 22: Multiplexers can be generalized to more data inputs inputs…
Multiplexers can be generalized to data inputs and select inputs
Also implemented as a tree of smaller multiplexers

## Slide 23: Lab: 4-input multiplexer
Design a multiplexer that switches one of the 4 input lines through a single output line using 2 lector bits.
X | Y | A | B | C | D | Q
0 | 0 | 1 | x | x | x | 1
0 | 1 | x | 1 | x | x | 1
1 | 0 | x | x | 1 | x | 1
1 | 1 | x | x | x | 1 | 1

## Slide 24: Solution:
X | Y | A | B | C | D | Q
0 | 0 | 1 | x | x | x | 1
0 | 1 | x | 1 | x | x | 1
1 | 0 | x | x | 1 | x | 1
1 | 1 | x | x | x | 1 | 1